## Slide 1: From thermal results to a FEMAP point cloud
How two scripts turn a 2-D transient thermal solution into a 3-D, vertex-centered point cloud you can map and visualize on a circular mirror.
npz_to_3D.py (Python) + show_point_cloud.bas (FEMAP API)

## Slide 2: The pipeline at a glance
Two inputs feed the Python mapper; its CSV feeds the FEMAP macro that draws the check.
Thermal model
model1_results.npz
Node map
model1_node_map.csv
npz_to_3D.py
map T -> nodes, build
vertex-centered circle
x, y, z, T
point-cloud table
show_point_
cloud.bas
FEMAP points
Result in FEMAP: geometry Points overlaid on the mirror model for a spatial sanity check.
Output flavors: a dense analysis cloud (~37k pts) and a fast viz skeleton (~600 pts).

## Slide 3: npz_to_3D.py — build the point cloud
SCRIPT 1

## Slide 4: What npz_to_3D.py does
Reads a transient thermal result and a node map, then writes a 3-D point cloud for one mirror at one time step.
INPUTS
OUTPUTS
Node map (.csv)
Cell centroids per plate: x_m, z_m, dx_m, dz_m
11 plates x 50 nodes (5 wide x 10 deep)
Thermal results (.npz)
T[timestep, node] = 773 x 550
t (time) and node_names arrays
Dense analysis cloud
Regular grid, clipped to the disk
<Mirror>_MirrorCloud3D_<t>s.csv (~37k pts)
Viz skeleton
Rim ring + a few rows/cols
<Mirror>_VizSkeleton_<t>s.csv (~600 pts)
Columns are always x, y, z, T — the table FEMAP reads as an arbitrary 3-D scalar map.

## Slide 5: The data it reads
Node map — geometry
Each row = a cell centroid with its size.
x = in-plane (uniform spacing dx).
z = through-thickness (fine near the surface).
Grouped by plate (mirror) name.
node_name links each row to its temperature column by NAME — robust even if ordering changes.
Results (.npz) — temperatures
773
time steps
550
nodes
T = [timestep, node] scalar field.
A chosen time snaps to the nearest step.
T is mapped onto the matching node name.

## Slide 6: The core idea: map the strip onto a centered disk
1. Rescale x to the true diameter
The mesh describes the shape of the field; x is scaled to the mirror's physical diameter L.
2. Center on the vertex
x_c = (x_m / X_mesh) * L - R, so the origin sits at the mirror vertex (0,0). R = L / 2.
3. Sweep y, clip to the circle
T is uniform in y, so keep points where x^2 + y^2 <= R^2; each takes T from its x.
x
y
vertex (0,0)
T varies across x, uniform in y

## Slide 7: Two clouds from one model
Same geometry and temperatures — different sampling for different jobs.
D
Dense analysis cloud
~37k
points (M1 @ 0.25 in)
Regular grid, clipped to the disk.
For the real scalar map in FEMAP.
S
Viz skeleton
~600
points (rim + rows/cols)
Outer rim + a few rows and columns.
Plots instantly for the geometry check.

## Slide 8: Built to fail loud — never a bad file
Every check runs before anything is written. On any failure: a clear message and no CSV.
1
Mirror only
M1-M7 accepted; others rejected by name
2
Names resolve
every node maps to a T column
3
Uniform dx
the rescale assumption is verified
4
No NaN / inf
temperatures and coordinates are finite
5
Inside the disk
x^2 + y^2 <= R^2 for every point
6
Centered + deduped
origin on the vertex; no coincident points

## Slide 9: Running npz_to_3D.py
1
Pick the node map .csv
2
Pick the results .npz
3
Choose output: dense / skeleton / both
4
Enter the time (seconds)
5
Type the mirror (e.g. M1)
6
Choose the output folder
You get
A 4-column CSV
x, y, z, T in inches
+ a summary
diameter, radius, point count, bounding box, T range, and any mesh-vs-CAD mismatch.

## Slide 10: show_point_cloud.bas — see it in FEMAP
SCRIPT 2

## Slide 11: What show_point_cloud.bas does
A FEMAP API macro that drops the cloud in as geometry Points — a placement check, one color.
1
Reads x,y,z,T
any delimiter; header and bad lines skipped; the T column is ignored
2
Places Points
one per row, single color, on their own layer (toggle in Visibility)
3
No re-mapping
the cloud is already centered and circular from Python
4
Safe by default
NextEmptyID never overwrites existing geometry; AppLock keeps it fast

## Slide 12: Landing the cloud on the real mirror
The CSV is in the mirror-LOCAL frame
Origin at the vertex, +Z along the optical axis — exactly how Python built it.
You enter the mirror's CSys
The macro transforms each local x,y,z to global with feCoordTransform, so the cloud sits on the right mirror in the right orientation.
Must be rectangular
Checked before anything is created; 0 = global.
mirror-local CSys
global
model
feCoordTransform

## Slide 13: Running it in FEMAP
1
File > Programming > API (Ctrl+F11), paste, Run
2
Enter the path to the x,y,z,T file
3
Enter the mirror's CSys ID (0 = global)
4
Points appear on layer 9100
Settings to tweak
PT_COLOR
palette index for the points
LAYER_ID
which layer to draw on
STRIDE
thin a dense file on the fly

## Slide 14: Generate -> visualize -> refine
THE LOOP
Python writes the cloud; the macro shows it in FEMAP; you confirm the fit and iterate.
Open items: measured diameters for M4-M7 are provisional (5.905 in), and M2's thermal span is wider than its CAD diameter — a data reconciliation on your side.