## Slide 1: Is the low first mode real?
Bearing stiffness modeling study: hand calcs ladder vs FEM, plus the duplex-spacing knob
f₁
Notes: Purpose: prove the low first mode isn't a modeling artifact before spending on stiffer bearings or geometry changes.

## Slide 2: Answer three questions before touching the bearing spec
1
What is actually moving?
Mode 1 strain energy by property. Bearings, housing, shaft, or joints.
2
What's the most a bearing could buy?
Bounding runs up to rigid bearings. If rigid misses, stop chasing bearings.
3
Is my modeling method honest?
Hand-calc ladder: CBUSH, seat attachment, and pair span checked against closed forms.
Only if bearings dominate the ESE and the rigid bound clears the requirement do stiffer bearings or a wider span earn the effort.

## Slide 3: Step 0: diagnose the full model first
ESE by property, mode 1
Bearings ≥ 50%: bearing value matters
Housing ≥ 30%: geometry / seat is the problem
Bearings < 20%: stiffer bearings won't help
Bounding runs
Bearings ×0.5, ×2, ×10, rigid
f ∝ kⁿ: n ≈ 0.5 bearing-controlled, n ≈ 0 insensitive
Rigid still below req → fix structure first
Model hygiene
Weight and CG vs CAD (CONM2 units, NSM)
Seat RBE2 vs RBE3 swap: does mode move > tol?
ORBIS preload state and double counting
Workbook tab: Diagnostics. Paste fractions and frequencies; the read-outs fill in automatically.

## Slide 4: The ladder: each FEM step has a closed-form twin
1
Cantilever
CBAR + tip CONM2, SPC base
Checks mesh, units, mass
2
CBUSH at base
Pair 6-DOF diagonal, coincident nodes
Compliance split: beam / radial / tilt
3
Plate + bore
3a RBE2 · 3b RBE3 · 3c modeled ring
Brackets seat attachment error
4
Spaced pair
Two CBUSHes at load centers
Sizes the spacing knob
Compare on the same six numbers every step: lateral, axial, torsional stiffness at the mass and the matching three modes. Statics first; modal disagreements are harder to debug.

## Slide 5: Steps 1–2: the bearing is a series spring
Lateral at the mass
1/k = L³/3EI + 1/Kr + L²/Kθ
Axial 1/k = L/EA + 1/Ka
Torsion 1/k = L/GJ + 1/Kt
f = (1/2π)√(k/m_eff), m_eff = M + 33/140·m_beam
Kt is your motor/brake hold, not the bearing. A bearing carries ~zero torque about its spin axis.
Chart: Share of lateral compliance (example inputs)
| Beam bending | Bearing tilt (L²/Kθ) | Bearing radial
Share of lateral compliance | 53.2 | 46.6 | 0.2
The tilt term carries the arm length squared. It's why tilt stiffness, and therefore pair span, usually dominates radial.

## Slide 6: Step 3: bracket the seat attachment
3a RBE2 at bore
Rigid hub. Has a closed form, so FEM must match it.
Upper bound
3b RBE3 at bore
Bore free to ovalize. No closed form; compare to 3a FEM.
Lower bound
3c Modeled outer ring
Real ring section bonded in bore. Truth sits here.
Between
Rigid-hub plate (outer edge clamped)
β = b/a, D = Et³/12(1−ν²)
Kθ = 4πD(1+β²) / [(1+β²)ln(1/β) − (1−β²)]
Ka = 16πD(1−β²) / a²[(1−β²)² − 4β²ln²β]
Kt = 4πGt / (1/b² − 1/a²) (in-plane)
Derived from the biharmonic solution and checked by strain-energy integration. Thin plate only (t/a < ~0.1).
Read: if 3a and 3b agree within tolerance, the attachment debate is over for this geometry. If they differ by 20%+, the real model needs 3c or a stiffened bore.
Set plate density to 0 in FEM: the hand calc treats the plate as massless.

## Slide 7: Step 4: spacing is a strong knob until it isn't
Chart: First lateral mode vs bearing center spacing (example inputs)
| 0.47 | 0.71 | 0.94 | 1.18 | 1.41 | 1.65 | 1.88 | 2.12 | 2.35 | 2.59 | 2.82 | 3.06 | 3.29 | 3.53 | 3.76 | 4.00
Hand calc | 88.2 | 97.6 | 104 | 108.6 | 111.9 | 114.4 | 116.3 | 117.7 | 118.9 | 119.8 | 120.6 | 121.2 | 121.7 | 122.2 | 122.6 | 122.9
Requirement | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150 | 150
Pair tilt stiffness
Kθ ≈ kr·s_lc²/2 + 2kθ
s_lc = s ± dm·tanα (+DB, −DF)
Goes with span squared, so the first half-inch buys the most
Plateaus once the overhang beam or housing owns the compliance (watch the 'tilt share' column)
In this example even 4 in can't reach 150 Hz: the arm is the limit
Notes: Example curve uses placeholder inputs from the workbook. Replace with ORBIS single-bearing values and your geometry.

## Slide 8: What spacing costs you
Preload becomes a tolerance stack
Split pair → preload set by inner vs outer spacer length match. Microns of mismatch shift preload a lot.
Thermal gradient eats preload
Shaft/housing CTE mismatch × span changes preload over temperature. Longer span, bigger swing. Run ORBIS hot and cold.
Housing becomes the limit
Two bores farther apart means a longer housing tube. Its bending now sits in series with the pair.
Load centers, not faces
DB spreads load centers outward by dm·tanα. Use ORBIS load-center span, not the drawing dimension.

## Slide 9: Acceptance criteria and decision rules
Check | Pass | If it fails
Steps 1, 2, 3a, 4 vs hand calc | Within 5% on k and f | Fix mesh, units, CBUSH coincidence before trusting anything
3a vs 3b (RBE2 vs RBE3) | Within 5% | Model the outer ring (3c) in the real model
ESE bearing share, mode 1 | ≥ 20% to justify bearing work | Spend on housing/geometry instead
Rigid-bearing bound | Clears requirement | No bearing or spacing can fix it
Spacing sweep, tilt share | Mode clears req before tilt share < ~15% | Arm/housing is the limit, not the pair
Tolerance and requirement are inputs in the workbook; the 20% and 15% thresholds are judgment calls, adjust to your error budget.

## Slide 10: Next steps
Run ESE and bounding runs on the full model, fill Diagnostics
Swap placeholders for ORBIS pair and single-bearing stiffness at operating preload
Build steps 1–3 in Femap, paste into FEM_Compare
If bearings own the mode: run the spacing sweep, then check preload hot and cold